## Slide 1: Sariya.
IQOO HACKATHON 2026 · GRAND FINALE · TOP TEAMS DEMO
Check the steel before the concrete hides it.
One phone and a printed card measure every bar in millimetres, offline on the NPU. The mason hears the fix in Hindi or Kannada; the engineer signs the record.
Alwin · Sabari · Melvin
Bengaluru · 11 Oct 2026

## Slide 2: The steel in a house is visible for a day or two. Then concrete hides it for good.
THE ONE-DAY WINDOW
Stirrups spaced evenly
where the drawing wants them tight at the beam ends.
A missing or swapped bar
a 10 mm bar where the drawing says 12.
Top steel trampled flat
no cover blocks, nothing over the supports.
Fixed tonight, or never
Minutes to fix tonight. After the pour, the only fix is a jackhammer.
Sariya · why this problem
2 / 5

## Slide 3: What the jury sees in the next three minutes
LIVE DEMO · HALF-SCALE PROPS, REAL 8 AND 12 MM STEEL · A JUDGE AT THE TABLE
0:20
The judge breaks the steel
Draws a fault card and applies it: removes a mesh bar, opens a gap to ~80 mm where the drawing says 50, or slides a stirrup out of the end zone.
0:45
Lines snap onto every bar, live
The judge slides a bar and its line and number follow. Lock: a verdict with values inside 3 s, spoken in Hindi, subtitled.
1:05
The judge checks us with a tape
On the exact segment the phone drew: "80 ± 5 mm". The band is on the screen before the tape comes out.
1:25
Honesty on show
From 0.8 m the phone says "move closer" and Lock is disabled. At 30 cm, a confident "outside limits".
2:10
The weigh test catches a swapped bar
A 200 mm offcut labelled "12" weighs 123 g. That is a 10 mm bar; a 12 would weigh 178 g (IS 1786).
2:30
The engineer signs from the desk
Engineer phone mirrored on the laptop over Office Kit: review, PIN, approve. A third phone verifies the QR offline. Yesterday's pack replayed: rejected.
Every phone is in airplane mode. The app checks whatever the drawing says; the half-scale props only halve the distances.
Sariya · the demo
3 / 5

## Slide 4: 12 ms a frame on the NPU, 19× faster than the CPU
BENCHMARK · IQOO 15 · SNAPDRAGON 8 ELITE GEN 5 · ONE 1152×640 FRAME · MEASURED ON THIS LOANER
CPU · XNNPACK
235
NPU · default mode
73
GPU · OpenCL
19.8
NPU · high performance
16.9
NPU · burst
12.2
NPU · pre-compiled file
11.6
33 ms = one camera frame at 30 fps
160 / 160
layers on the Hexagon NPU, one partition, float model, no quantisation yet
12.8 ms sustained
average over 60 s, 4,692 runs; skin 32.7 → 39.8 °C, no throttling
53 s → 133 ms
start-up: the on-phone compile replaced by a pre-compiled NPU file (LiteRT 2.3, QAIRT 2.50)
~65 ms a frame
in the app: camera, card pose, model and geometry. Other phones fall back to GPU, then CPU, and the readiness screen says which
Sariya · the phone · values in ms, V1 shown; V3 runs 12.1 ms in burst
4 / 5

## Slide 5: Sariya measures and records. The engineer certifies.
SARIYA · THE ASK
One steel or cement brand
An introduction to a technical-services team in Bengaluru for a 60-pour pilot from November.
One structural engineer
To sign off the rulebook's spacing tolerances, which IS 456 leaves open.
Three iQOO 15s on real sites
The phone whose NPU makes a live, offline measurement loop possible at zero marginal cost.
Alwin · Sabari · Melvin · github.com/Melvin0070/sariya
5 / 5

## Slide 6: One card, offline: the whole pour loop, scan to signature
WHAT WE BUILT · RUNNING ON THE IQOO 15 · AIRPLANE MODE THROUGHOUT
01 · Engineer phone
Sends the drawing values, signed
Bar size, spacing, stirrup zones, cover. Signed with a PIN. The app never invents a value.
02 · Operator phone
Scans live, lines on every bar
The printed card gives true scale. Gaps show in mm as you move. Lock fuses ~1.2 s of sharp frames into one value with its band.
03 · Rulebook
Decides, or says re-scan
Drawing first, then IS 456 and IS 13920 by zone. Within limits, outside limits, needs a tape reading, or re-scan. Never "safe".
04 · By hand
Asks for what a camera can't see
Cover by tape. Diameter by weighing a 200 mm offcut against IS 1786 bands. Hooks by template, only where the drawing asks.
05 · The mason
Hears the fix in Hindi or Kannada
"Gap 3 is 100 mm. Drawing says 50 mm. Add 1 bar in gap 3." Spoken offline, subtitled, repeatable.
06 · Signed record
Engineer approves from their desk
Two phones, two keys. Reviewed on the laptop over Office Kit. Sign-off QR verifies offline. Replays and edits are rejected.
Sariya · the product
Backup B1

## Slide 7: AI finds the bars. Maths measures them. Rules decide.
HOW IT WORKS · ONE MODEL IN THE CAMERA LOOP, EVERYTHING ELSE IS MATHS AND RULES
Camera
CameraX preview and analysis at 1920×1080, torch on, blurred frames dropped
AI
U-Net + MobileNetV3 segments bar pixels on the Hexagon NPU: 12 ms a frame, every frame
Maths
ChArUco card pose (OpenCV) gives a homography; the mask is warped into the card plane, in mm
Maths
Bar lines from an offset profile; Lock fuses ~15 still frames into count and gaps, each with a band
Rules
Versioned rulebook: the drawing, then IS 456, IS 13920 by seismic zone. Plain code, unit-tested, auditable
Model output on a real rebar test photo never seen in training (IoU 0.94 on this image). Card pose, lines, millimetres and verdicts come from maths, so they never hallucinate.
~65 ms
whole frame in the app
Offline
no cloud calls
1 model
with one narrow job
Sariya · how it works
Backup B2

## Slide 8: Re-scan, never guess
DESIGNED TO ABSTAIN · WHAT HAPPENS WHEN THE MODEL IS WRONG
GEOMETRY ON A KNOWN MESH
Measured, mm
50.1 · 49.9 · 64.9
Truth, mm
50 · 50 · 65
Card-S mesh with known positions, the app's own geometry. Every locked value carries a band with a 5 mm field floor; the tape table on real steel grows with every pour.
Within its own band of the limit
says re-scan, not "outside". 68 ± 5 mm against a 65 limit says re-scan; 72 ± 5 is outside.
Blurred frame
dropped. Sharpness is judged against the best recent frame of the same scan, so nothing needs calibrating per camera.
Bar only partly seen
drawn dashed, never counted. A short count or a wide gap that touches one turns into re-scan, not "add a bar".
Too far from the card
"Move closer", Lock disabled. Only locked, quality-gated evidence ever reaches the rulebook.
Words it never says
"Safe", "certified", "PASS", "pour permit". It reports numbers, bands and evidence. The engineer certifies.
Sariya · how it works
Backup B3

## Slide 9: Two phones, two keys: a record the engineer signs from their desk
TRUST · OFFICE KIT IS THE ENGINEER'S DESK
Engineer phone
Issues the drawing values
Signed with the engineer's key behind a PIN. The operator's phone accepts them only from an enrolled key.
Operator phone
Captures and signs
The capture binds locked values, spec revision, model, rule and calibration versions, image hashes and a coverage map. Ed25519, one key per phone.
Laptop · Office Kit
Reviews and approves
Pack travels as a file; the engineer phone is mirrored on the laptop. Approve, or send "fix and re-scan" with the same sentence the mason hears.
Any enrolled phone
Verifies the QR offline
The owner, the lender or the brand checks the sign-off against enrolled keys, with the full evidence pack one tap away.
Tamper-evident, not tamper-proof
Edit a signed value and the signature drops; the review shows "typed on site".
Replay yesterday's pack: "already processed". Same key cannot approve its own capture.
Values that differ from what the engineer signed block approval.
Built for the engineer with many sites
Pour inbox: sites sorted by what needs a decision, then the next pour.
Fix loop on both phones: "widest gap 80 ± 5 → 50 ± 5 mm, closed".
Slab, beam and column members; Hindi, Kannada and English fixes.
Sariya · trust
Backup B4

## Slide 10: Everyone agrees the steel must match the drawing. Between visits, nobody measures it.
SITE VISIT · SMALL TO MID-SIZE HOUSE · BENGALURU · 9 OCT
THE COST
₹5–10k
per engineer visit, quoted on site. Small houses skip it, or stretch one visit across many pours.
WHAT THE CREW SAID
“Exactly as drawn”
Any deviation gets corrected until it matches. Only the engineer clears the pour.
WHAT WE SAW
Errors in the steel
Mistakes the crew themselves said the engineer would not accept. Nobody had measured yet.
55–57% of India's cement goes into housing
CRISIL, FY25. Rural housing alone is 32–34%.
Liability is moving onto the engineer
Bengaluru's Nambike Nakshe: professionals self-certify plans. Taratala, June 2026: the structural engineer was arrested.
Today's check: a tape and a WhatsApp photo
Nothing measured, nothing recorded, nothing signed. One site, first-hand. We do not quote it as a statistic.
Sariya · why this problem
Backup B5

## Slide 11: Three rounds of fine-tuning, measured on the same held-out sets
AI RESEARCH · OPEN WEIGHTS, PUBLIC DATASETS, KAGGLE T4, TIMESTAMPED LOGS AND DATASET HASHES IN THE REPO
Same test sets | V1 | V2 | V3 · in the app
Trained on | 1,555 real photos | +1,100 negatives | +2,500 stirrup scenes
Test IoU (ROI-1555) | 0.846 | 0.811 | 0.851
Precision / recall | 0.876 / 0.951 | 0.930 / 0.870 | 0.921 / 0.919
False alarms, no-rebar tiles | 80% | 0% | 0%
Recall, 233 real stirrup photos | – | 0.873 | 0.910
NPU latency, iQOO 15 | 12.2 ms | 11.6 ms | 12.1 ms
Why U-Net + MobileNetV3, and not an off-the-shelf detector
Full-resolution masks for 9-pixel bars; MIT and Apache weights. YOLO-seg is faster on paper (2–3 ms) but gives quarter-resolution masks under AGPL; DeepLabV3+ smears thin bars; MobileSAM takes 500–750 ms. The exported phone model matches PyTorch on 100% of mask pixels.
V1: cables read as bars
V2: nothing marked, 0.0%
Same desk, same phone, live on the NPU. Removing false alarms cost real bars; V3 won recall back with varied data, not more epochs.
Sariya · the model
Backup B6

## Slide 12: Japan validated the physics in 2023. We rebuilt it for India's self-built pour.
NOVELTY · PRIOR ART WE LEAN ON, AND WHAT IS NEW
 | Japan: IHI, AIJO, Kajima and others, MLIT-accepted since July 2023 | Sariya
Who checks | Contractor QA teams on large sites | The person paid to check a house the evening before the pour; a remote engineer signs
Where it runs | Tablet or PC, cloud workflow, stereo or LiDAR at the high end | One phone, fully offline, the model on the NPU
Rules | Japanese codes; 5 mm guide on spacing | The drawing, IS 456, IS 13920 by zone; an error band and "re-scan" on every number
Bar sizes | 3 mm steps (D10, D13, D16) judged from images | 2 mm steps (8, 10, 12): diameter from a weighed 200 mm offcut against IS 1786, which also catches underweight steel
Who hears it | A QA report in Japanese | The mason, in Hindi or Kannada; the engineer, as a two-key signed record
Not new: measuring rebar with a camera. Japan ships it, and that is why we trust the physics.
New: where it runs and whom it serves. We found no phone-based pre-pour rebar measurement product in India; brand visits, builder checklists and inspectors all photograph, none measures.
Sariya · novelty · MLIT guideline 2023; IHI ±1 mm diameter, ±5 mm spacing; AIJO 70% time saved
Backup B7

## Slide 13: Who pays: whoever already sends a paid person to the pour
BUSINESS · STEEL BRANDS FIRST · THE UNIT IS THE SIGNED POUR RECORD
1
Steel brands
A "missing bar" finding sells steel. The scan verifies their brand on site and gives the dealer the slab date 24–48 h ahead. Sponsor the record for their customers.
2
Cement technical services
Already at the pour for free: Ambuja supervised slab casting at 31,698 sites in a year. The visit becomes a branded, signed report and more sites per engineer.
3
Builders, engineers, inspectors
Per record, resold to the owner as a pre-pour report. Owners already pay ₹4,999 a visit (TeamHome) and ₹5–10k an engineer visit.
4
Lenders and insurers, year 2
Buy the evidence layer only: a signed stage pack for tranche release (borrowers pay ₹750–1,500 a visit today) and for inherent-defects cover.
SIZING · OUR ARITHMETIC, PILOTS WILL TEST IT
~8M
RCC slab pours a year in India (range 5–12M), from ~10M new dwellings and cement tonnage
₹99–299
per signed record, against ₹5–10k for one engineer visit
₹200 Cr
a year software TAM at ₹250 a record; Bengaluru beachhead 25–50k pours
Inference never leaves the phone, so the marginal cost of a record is a printed card. Value in Indian construction accrues to materials platforms; Sariya is built to be the trust instrument a steel brand embeds.
Sariya · business · prices are hypotheses; no partner has agreed yet
Backup B8

## Slide 14: Next 90 days: three Bengaluru pilots and one growing error table
NEXT · 12 OCT 2026 TO 10 JAN 2027
Pilot A · brand technical team
3–5 engineers, 60 pours
Minutes per member; agreement with tape (target ≤ 5 mm spacing error, ≥ 98% count); share of checks outside limits. Success: used unprompted at 70% of pours by week 8.
Pilot B · organised builder
QC supervisors, 20–30 pours
A measurement module inside their checklist, the signed record attached to the stage payout. Success: a rebar step written into their SOP and a 2027 per-site price.
Pilot C · inspector
A new SKU: pre-pour steel check
15–20 paid visits at ₹2,999–4,999 with a second engineer grading the reports. Success: 10 paid visits and the SKU listed publicly.
Product after the pilots
Photograph the bar-bending schedule to pre-fill the spec, every field confirmed.
Per-site registered cards and a hash-chained site log for self-certifying engineers.
Device-bound biometric keys; one-tap PDF to WhatsApp with the verify QR.
What we will not claim until measured
Accuracy on real steel beyond our tape table; the band stays at a 5 mm floor until it earns less.
Defect rates: no "N of M sites" statistic exists in India yet. Pilot A produces the first one.
Diameter from a standing scan. The scale decides, by design.
Sariya · what's next
Backup B9

## Slide 15: Built in 48 hours, all code written at the event
TEAM · VISION, ANDROID AND TRUST ENGINEERING, TOGETHER 3+ YEARS
Alwin
UI and UX
Every screen, the live overlay, the manual-mark fallback, Hindi and Kannada output, the review desk and the pour inbox.
Sabari
Vision and AI
Three model rounds on Kaggle, the NPU runtime through LiteRT and QAIRT, card calibration, live bar geometry and Lock uncertainty.
Melvin
Rules, trust, integration
The IS rulebook, signed captures and approvals, key enrolment, replay policy, Office Kit transport and the release build.
Know this phone
Built a local AI agent on the same iQOO 15 at the Chennai City Battle. Nothing from it is reused here.
Ship AI products for a living
Production features at Xavier AI, LiveAltLife, Kalvium Labs and Montra Electric. 3+ years and 3+ state-level TinkerHub wins together.
Did the homework
The idea survived an adversarial red team and a six-idea comparison. Every number on these slides has a graded source in the repo.
Sariya · team · open weights attributed; OpenCV, LiteRT and public datasets disclosed
Backup B10